PowerSupplySimu.db

# records for EPICS Training at 19. Nov. 2010

#------------------------------------------

# interface records

record (bo, "PowerSupply1:Switch")

{

field (DESC, "Switch On or Off")

field (ZNAM, "Off")

field (ONAM, "On")

field (FLNK, "PowerSupply1:Calculation")  # after switch set calc output

}

record (ao, "PowerSupply1:SetValue")

{

field (DESC, "Nominal set value")

field (EGU,  "V")

field (PREC, "2")

field (FLNK, "PowerSupply1:Calculation")  # after switch set calc output

}

record (ai, "PowerSupply1:Readback")

{

field (DESC, "Actual readback from HW")

field (EGU,  "V")

field (PREC, "2")

field (INP,  "PowerSupply1:OutputValue")

field (SCAN, ".1 second")

}

#------------------------------------------

# private records (do not use them on clients)

record (calc, "PowerSupply1:Calculation")

{

field (DESC, "Combine Switch and SetValue")

field (INPA, "PowerSupply1:Switch")

field (INPB, "PowerSupply1:SetValue")

field (CALC, "A=0?0:B")  # if switch=Off then Null else setValue

field (FLNK, "PowerSupply1:OutputValue")  # after calculation write output

}

record (ao, "PowerSupply1:OutputValue")

{

field (DESC, "Value send to HW")

field (EGU,  "V")

field (PREC, "2")

field (DOL,  "PowerSupply1:Calculation")  # get the output value

field (OMSL, "closed_loop")

}

st.cmd

# Load drivers and dbd files ==============

# Load your record files ==================

dbLoadDatabase("PowerSupplySimu.db")

# this is a comment...

#dbLoadTemplate("PowerSupplySimu.subs")

# start the EPICS IOC =====================

iocInit

PowerSupplySimu.subs

#--------------------------------------------------------------------

# records for EPICS Training at 19. Nov. 2010

file PowerSupplySimu.template {

{

Name = PowerSupply1

}

{

Name = PowerSupply2

}

}

PowerSupplySimu.template

# records for EPICS Training at 19. Nov. 2010

#------------------------------------------

# interface records

record (bo, "$(Name):Switch")

{

field (DESC, "Switch On or Off")

field (ZNAM, "Off")

field (ONAM, "On")

field (FLNK, "$(Name):Calculation")  # after switch set calc output

}

record (ao, "$(Name):SetValue")

{

field (DESC, "Nominal set value")

field (EGU,  "V")

field (PREC, "2")

field (FLNK, "$(Name):Calculation")  # after switch set calc output

}

record (ai, "$(Name):Readback")

{

field (DESC, "Actual readback from HW")

field (EGU,  "V")

field (PREC, "2")

field (INP,  "$(Name):OutputValue")

field (SCAN, ".1 second")

}

#------------------------------------------

# private records (do not use them on clients)

record (calc, "$(Name):Calculation")

{

field (DESC, "Combine Switch and SetValue")

field (INPA, "$(Name):Switch")

field (INPB, "$(Name):SetValue")

field (CALC, "A=0?0:B")  # if switch=Off then Null else setValue

field (FLNK, "$(Name):OutputValue")  # after calculation write output

}

record (ao, "$(Name):OutputValue")

{

field (DESC, "Value send to HW")

field (EGU,  "V")

field (PREC, "2")

field (DOL,  "$(Name):Calculation")  # get the output value

field (OMSL, "closed_loop")

}

PowerSupply.subs

#--------------------------------------------------------------------

# records for EPICS Training at 19. Nov. 2010

#file PowerSupplySimu.template {

#	{

#	Name = PowerSupply3

#	PLC = PLC1

#	}

#}

file PowerSupply.template {

pattern {Name               PLCname }

{PowerSupply3       PLC1    }

}

PowerSupply.template	page 1

# records for EPICS Training at 19. Nov. 2010

#------------------------------------------

# interface records

record (bi, "$(PLCname):Status")

{

field (DESC, "Is PLC online?")

field (ZNAM, "offline")

field (ONAM, "online")

field (ZSV,  "MAJOR")  # alarm when offline

field (DTYP, "S7plc stat")

field (INP,  "@$(PLCname)")  # read from PLC

field (SCAN, "I/O Intr")

field (PINI, "YES")

}

record (bi, "$(PLCname):Watchdog")

{

field (DESC, "Blinks when PLC works")

field (ZNAM, "Off")

field (ONAM, "On")

field (DTYP, "S7plc")

field (INP,  "@$(PLCname)/8 T=BYTE B=7")  # read from PLC

field (SCAN, "I/O Intr")

}

record (bo, "$(Name):Switch")

{

field (DESC, "Switch On or Off")

field (ZNAM, "Off")

field (ONAM, "On")

field (FLNK, "$(Name):Calculation")  # after switch set calc output

}

record (ao, "$(Name):SetValue")

{

field (DESC, "Nominal set value")

field (EGU,  "V")

field (PREC, "2")

field (FLNK, "$(Name):Calculation")  # after switch set calc output

}

record (ai, "$(Name):Readback")

{

field (DESC, "Actual readback from HW")

field (EGU,  "V")

field (PREC, "2")

field (DTYP, "S7plc")

field (INP,  "@$(PLCname)/4 T=FLOAT")  # read from PLC

field (SCAN, "I/O Intr")

}

PowerSupply.template	page 2

#------------------------------------------

# private records (do not use them on clients)

record (calc, "$(Name):Calculation")

{

field (DESC, "Combine Switch and SetValue")

field (INPA, "$(Name):Switch")

field (INPB, "$(Name):SetValue")

field (CALC, "A=0?0:B")  # if switch=Off then Null else setValue

field (FLNK, "$(Name):OutputValue")  # after calculation write output

}

record (ao, "$(Name):OutputValue")

{

field (DESC, "Value send to HW")

field (EGU,  "V")

field (PREC, "2")

field (DOL,  "$(Name):Calculation")  # get the output value

field (OMSL, "closed_loop")

field (DTYP, "S7plc")

field (OUT,  "@$(PLCname)/4 T=FLOAT")    # write to PLC

}

st.cmd

# Load drivers and dbd files ==============

dlload /opt/epics-3.14.12/modules/lib/linux-x86/libs7plc.so

dbLoadDatabase /opt/epics-3.14.12/modules/dbd/s7plc.dbd

s7plc_registerRecordDeviceDriver

# Configure the hardware

#s7plcConfigure "PLCname","IPaddr",IPport,inSize,outSize,bigEndian,recvTimeout,sendIntervall

s7plcConfigure "PLC1","192.168.0.10",2000,10,10,1,500,100

# Load your record files ==================

dbLoadTemplate("PowerSupply.subs")

# start the EPICS IOC =====================

iocInit